# Specification Text

## Automatic Sliding Door

Dimensions

Overall width		........... mm

Overall height		........... mm

Passage width		........... mm (800 – 3800 mm)

Passage height		........... mm

## TORMAX iMotion® 2202 Sliding Door Drive

Automatic sliding door drive for single or double-leaf sliding doors, standard or telescopic.

- Max. door leaf weight 1 x 130 kg, 2 x 120 kg, telescope 4 x 80 kg, 2 x 80 kg.

- Cross section header profile (H x D) 100 x 142 mm, telescope 100 x 204 mm

- In compliance with current European standards

( _ )	Electromechanical sliding door drive with wear-free synchronous motor technology and processor control. Mains supply 115 VAC/60 Hz or 230 VAC/50 Hz

- Protective system IP22, ambient temperature –20 °C to +50 °C. 
RoHS conformity (EC directive 2002/95/EG).

- Easily replaceable noise-damped guide rail.

- Integrated cable duct and integrated concealed sealing brushes.

- Mounting method: Lintel mounting, wall mounting, ceiling mounting.

- Tested by TÜV and certified according to EN IEC 60335, DIN 18650: 2010, 
EN ISO 13849: 2008 Performance level „d“.

- Control System
Automatic detection of system-specific data for optimal motion control, permanent operating diagnosis.

- Electronic obstacle recognition in closing and opening directions, adjustable reversing sensibility

- Automatic speed limit, including in the event of power failure and in manual mode.

- Emergency opening for autonomous door opening in the event of power failure in the unlocked state.

- 32 Bit/30 MHz processor for high performance.

- Interfaces: LIN BUS, CAN BUS, RS 232

- Fault recognition, display and log.

- Air-lock-function

- User interface with fault diagnosis and code lock. Selectable operating modes: OFF, AUTOMATIC 1, AUTOMATIC 2, EXIT , OPEN and MANUAL. 
Freewheeling function and reset selectable on operating unit.

- 8 inputs (4 testable safety devices)

- 3 programmable outputs (optional feedback signals for different door statuses, 
such as: Closed, Open, Fault, Lock status, Light pulse, Gong pulse).

- Modular extendable by max. 2 I/O-modules (4 in-/outputs each)

- Integration in higher-level system possible, e.g. a building management system, optionally via potential-free contacts or a bus system

## Door leaves

( _ )	Sliding leaf

( _ )	Stationary lateral components

( _ )	Stationary fanlights,     ( _ ) -part

Profiles

( _ )	TORMAX Profile System LR 12

Single-sheet glazing

Glazing thickness 6 – 12 mm

Type of glazing: wet, single-sheet/compound toughened safety glass

Facial width 22 mm, base height 80 mm, profile depth 20 mm

( _ )	TORMAX Profile System LR 22B

Single-sheet and insulating glazing

Glass thickness dry 8.5 – 10 mm, 21.5 – 23 mm, wet 6 – 28 mm

Facial width 30 mm, base height 78 mm, profile depth 34 mm

( _ )	TORMAX Profile System LR 32THERM

Insulating glazing

Glazing thickness max. 32mm,

Facial width 35mm, base height 85mm, profile depth 40mm

( _ )	Make…………

Floor guide

( _ )	Continuous floor guide in CNS, including glider in the sliding leaf

( _ )	Continuous floor guide in aluminium anodised E6/EV1 incl. gliding piece in sliding leaf

Colour of visible profiles

Elox anodising colour	…………….

Powder coating RAL	…………….

…………….…………….………………..

Glazing

( _ )	Single-sheet safety glass 10 mm, heat soak tested

( _ )	Compound safety glass 10 mm, with 0.78 mm film

( _ )	Insulating glass comprising 2 x 5 mm single-sheet safety glass, heat soak tested, 22 mm

Overall thickness, Ug 1.3 W/m2K

( _ )	Insulating glass comprising 2 x 6 mm compound safety glass, film 0.78 mm, 22 mm

Overall thickness, Ug 1.3 W/m2K

( _ )	Double insulating glass comprising 2 x VSG, overall thickness 31.1mm, Ug 1.0W/(m2/K)

( _ )	Triple insulating glass comprising 3 x ESG, overall thickness 32mm, Ug 0.8W/(m2/K)

( _ )	Make…………

## Sensors

Activation

( _ )	Radar

( _ )	Active infrared

( _ )	Passive infrared

( _ )	Contact-free hand switch

( _ )	Manual hand switch

Safety facility

( _ )	Dynamic safety (with/without testing)

( _ )	Static safety (with/without testing)

( _ )	Combined detector/alarm (radar and 3D protective light curtain AIR) with testing

Safety assessment conforming to DIN 18650 recommended. A declaration of conformity of the door system is mandatory in the area of validity of the machine guidelines 98/37/EG.

## Accessories

( _ )	User interface with 6 operating modes and fault display, 45 x 45 mm suitable for Legrand system

( _ )	3-position operating mode switch mounted in plastic case

( _ )	Monitored battery module for emergency power supply

( _ )	Electromechanical lock (bistable lock) with feedback, acting only on hardened holding bolts of the leaf, not acting on the toothed belt or deflection pulley

( _ )	Emergency opening including burglary protected emergency unlocking

( _ )	Emergency opening monitoring facility

( _ )	Emergency OFF switch, optionally surface-mounted or flush-mounted, 
with glass cover and frame

( _ )	Integration in system network with contacts communication

( _ )	Integration in system network with bus communication