# Specification text

## Automatic swing door

Dimensions

Overall width		........... mm

Overall height		........... mm

Passage width		........... mm

Passage height		........... mm

## TORMAX iMotion® 1401 Swing Door Drive

Concealed floor-mounted drive for swing doors, simultaneously usable as lower door bearing. Door leaf weight up to 450 kg with 1 m leaf width.

( _ )	Electromechanical swing door drive with wear-free synchronous motor technology and processor control system, extremely quiet running. Dimensions L x W x D: 
450 x 293 x 127 mm, door leaf weight up to 450 kg for 1 m leaf width (J = 150 kgm2), protective system IP 67 (7 days water up to top edge of housing), 
power supply: 1 x 230/115 V AC 50 – 60 Hz, 
power consumption: 4 - 250 W, ambient temperature –20 °C to +50 °C, 
integrated adjustable end-stop for door-closed position, integrated spring-loaded and adjustable end-stop in the opening direction.

Control system

Control box locatable independently of drive, protective system IP 55, ultra-simple commissioning by "teach-in" learning run, "push and go", high personal safety due to built-in reversing system and external monitored safety, safe closing due to motor power assist even under the most awkward conditions (wind load), power-free closing, in the event of power failure simple manual operation without disconnection, door closer function in the event of power failure, hold-open time: 0 – 600 s, opening angle 0 – 99°, 8 inputs and 2 outputs (freely programmable).

Floor sealing

( _ )	Flush-mounted in-floor mounting frame for floor covering up to 20 mm thick with extended drive shaft

( _ )	Stainless steel cover plate with seal fitted on floor, 
L x W x H = 480 mm x 320 mm x 3.5 mm

Power transmission: drive to door

( _ )	Drive shaft with serrations and specific shaft end made to order

( _ )	Drive shaft with serrations and cone designed to fit stainless steel cover 1401

( _ )	Drive shaft with serrations and cone designed to fit floor covering

( _ )	Drive shaft with serrations and unprocessed shaft end, length 164.5 mm

( _ )	Noise-insulated door arm for centrally borne DIN R & DIN L doors with panic system

( _ )	Noise-insulated door arm for eccentrically borne doors, offset 
(dimension k (max. 70 mm)) according to customer specification

( _ )	Noise-insulated panic door arm for centrally borne DIN R & DIN L doors, with panic system

( _ )	Basic drive shaft connecting piece door arm fitting shaft with end cone, 
L x W x H = 102 mm x 30 mm x 35 mm, including 2 spacer plates

## Sensors

Activation

( _ )	Radar

( _ )	Active infrared

( _ )	Passive infrared

( _ )	Contact-free hand switch

( _ )	Manual hand switch

Safety facility

( _ )	Dynamic safety (with/without testing)

( _ )	Static safety (with/without testing)

( _ )	Combined detector/alarm (radar and 3D protective light curtain AIR) with testing

Safety assessment conforming to DIN 18650 recommended.

## Accessories

( _ )	User interface with 7-segment display and 2-button operation, 45 x 45 mm suitable for Legrand system

( _ )	3-position mode switch mounted in plastic case 
45 x 45 mm, suitable for Legrand system

( _ )	Bowden wire switch

( _ )	Radio remote control, receiver integrated in switch cabinet, including mini manual transmitter, 4-channel, 868 MH

( _ )	Emergency OFF switch, flush-mounted, with glass cover and frame

( _ )	Monitored battery module for emergency current supply (battery backup)