# Specification text

## Automatic swing door

Dimensions

Overall width		........... mm

Overall height		........... mm

Passage width		........... mm

Passage height		........... mm

## TORMAX Smart Drive 1101

Drive for swing doors, for internal doors, lintel or door leaf mounting, 
optionally DIN L and DIN R doors.

( _ )	Electromechanical swing door drive with ball screw, DC motor and processor control, dimensions 85 x 116 x 580 mm, integrated robust open end-stop, 
power supply: 1 x 230/115 V AC 50 – 60 Hz, power consumption: 3 – 140 W, motor-driven opening, spring-loaded closing, integrated open holding, integrated open end-stop, acting as power-free door closer with motion control.

Control system

Ultra-simple commissioning due to manually guided "teach-in" learning program.
Two independent motional sequences can be set and controlled, adjustable hold-open time – satisfies low-energy requirement, obstacle recognition (reversing) in both opening and closing directions, automatic opening by manual pushing or pulling ("push and go" function), safety features can be monitored, feedback signal for door in open or closed position, 6 programmable inputs, 3 programmable outputs.

Power transmission: drive to door

( _ )	Standard linkage, infinitely variable, pushing, for lintel depth 40 ... 107 mm

( _ )	Standard linkage, infinitely variable, pushing, for lintel depth 105 ... 252 mm

( _ )	Sliding lever pulling

( _ )	Sliding lever, pulling, with panic fitting

( _ )	Connecting shaft, drive – linkage, L = 63 mm (mounting flush with lintel)

( _ )	Connecting shaft, drive – linkage, L = 82 mm (mounting flush with lintel)

( _ )	Connecting shaft, drive – linkage, L = 123 mm (mounting flush with lintel)

## Sensors

Activation

( _ )	Radar

( _ )	Active infrared

( _ )	Passive infrared

( _ )	Contact-free hand switch

( _ )	Manual hand switch

Safety facility

( _ )	Dynamic safety (with/without testing)

( _ )	Static safety (with/without testing)

( _ )	Combined detector/alarm (radar and 3D protective light curtain AIR) with testing

Safety assessment conforming to DIN 18650 recommended.

## Accessories

( _ )	3-position mode selector switch, operating modes: Door closed, Automatic operation, Permanently open

( _ )	Bowden wire switch

( _ )	Monitored battery module for emergency current supply (battery backup)

( _ )	Continuous casing over the full door width

( _ )	Cable set for master/slave connection