| PRODUCT | TVR61 High Performance Brass Check Valve |
| --- | --- |
| URL | http://www.ac-fluid.co.uk/p-246/High-Performance-Brass-Check-Valve-TVR61.aspx |
| MAIN PICTURE |  |
| PICTURE GALLERY |  |
| INTRODUCTION | The TVR61 brass valves are robust well proven designs for hydraulic and pneumatic media in applications such as heating systems, air conditioning systems, plant engineering, submersible pumps, pressure lines and many other applications. The valves have a high flow rate, operate in any position and are virtually silent. Internal threads are available on both inlet and outlet for standard dimensions from G1/4" up to G2". Other connection versions and sizes are available on request. |
| STANDARD DATA | High flow rate Virtually silent Robust and long lasting Compact design 0.025 bar cracking pressure 48 bar maximum operating pressure DN: 10 mm up to 50 mm Minimum pressure loss |
| DOWNLOADS | Datasheet – TVR61 High Performance Brass Check Valve. |